## Slide 1: Esri Prepares for 2022
Melita Kennedy

## Slide 2: Preparation
Engaging with NGS
Webinars
Geospatial Summits
Personal communication
Customer communication
Testing when data is released
Notes: My colleague, Kevin Kelly, and I are engaged with NGS. We’ve both been attending the webinars--live when we can or certainly once the webinar recordings are published. Kevin has been or will be attending the Geospatial Summits hosted by NGS and certainly we will respond or collaborate on any invitations made to industry partners. We have been contacted by customers who have heard about 2022 usually asking, “When will you support the new datum?” We will support them as soon as possible after they are released officially by NGS.
NGS plans to release a beta version. We will commence testing and writing documentation the data so that it can be incorporated into the next software versions after the official release.

## Slide 3: What does it mean to “add support”?
CRS and transformations are added to the projection engine
New methods like interpolation method must be added
File formats must be supported
We already support GEOCON and Vdatum file formats
Notes: What does it mean when I say we’ll “add support”?
Coordinate reference systems and transformations are stored in the Esri projection engine library. The library also includes the projection and transformation methods. If any new method like an interpolation method is required, we would need to implement it. If a transformation requires on-disk files, we need to support the file format as well. We do support the GEOCON and Vdatum file formats already, so if the 2022 transformations use the same or similar format, it won’t take us long to implement them.

## Slide 4: Incorporating State Plane, UTM, other CRS
NGS-created ones we will add when published
State-created ones
  Contact Technical Support
  Me (mkennedy@esri.com)
Contact EPSG
  http://www.epsg.org
  To request addition, must register for an account
  Information is not shared beyond EPSG
I am happy to help
Notes: Adding projected CRS can happen by three methods. Anything published by NGS will be added when it’s finalized. States can define their own, for instance low-distortion systems. You can contact Technical Support or me directly at mkennedy@esri.com and I’ll work with technical support to get the proper change requests/issues entered. Everything that Esri receives, I will try to also ask whether you can submit the information to the EPSG or whether I can do it. I’m a member of the group that maintains it and will be happy to help.
What’s the difference between whether Esri adds it or we add it from the EPSG Dataset? Every CRS and transformation has a unique identifier. An object added by Esri will have an Esri ID so it may not be understood by other software. Many GIS software do support EPSG IDs and data, so the object is likely to be understood by more software and will have improved interoperability.

## Slide 5: Data Files
ArcGIS Coordinate Systems Data setup
Can be re-used for Desktop, Pro, etc.
Tied to a release
Want to update ArcGIS Pro but not Desktop?
  Install the latest CSD setup
  It will work with the previous Desktop version
Notes: Data files that are needed by transformations are no longer added to the core setup programs. For the last few releases, we now have an ArcGIS Coordinate Systems Data (CSD) setup. The same set of installed files can be used by ArcGIS Desktop and Pro. The setup is tied to a release but we are trying to release once per ArcGIS Desktop and Pro releases. For instance, we are using the same set of files for ArcGIS Pro 2.3 and the upcoming ArcGIS Desktop 10.7.
If you have multiple software installed on a machine, you can update one plus its CSD setup and the other software will just ignore the new data.

## Slide 6: Documentation
Static versus dynamic datums/GeoCRS
Update and add transformation methods
Which transformations should be used?
ArcGIS Pro
  Add geodetic topics
  Show transformation details
Notes: We are planning to update to our documentation this year—particularly adding more geodetic topics like discussing static/classic versus dynamic datums/Geographic CRS.
Update and add information on transformation methods
More topics on which transformation should you use.
ArcGIS Pro has very little documentation on coordinate systems and transformations. We want to expand that. An idea for improving the user interface is to allow direct access to the details of a transformation like: method, parameters, area of use, and accuracy.