## Slide 1
Dr. Byron Smiley • 30 Jan 2019
Methods and Results
ON-ORBIT GEOMETRIC CALIBRATION OF A SKYSAT

## Slide 2
SkySat constellation update/review
On-orbit geometric calibration techniques:
  boresight definition, using Landsat 8 PAN as reference
  interior orientation, using Pléiades-1A/B as reference
Outline
Featuring real SkySat-14 data!

## Slide 3
SKYSAT CONSTELLATION UPDATE

## Slide 4
Planet currently has 15 SkySats in orbit
SkySat-1
launched on Dnepr, 21 Nov 2013
~570 km, 11:02am (as of Jan 2019)
SkySat-2
launched on Soyuz, 8 Jul 2014
~620 km, 3:09pm (as of Jan 2019)
SkySat-3
launched on PSLV, 22 Jun 2016
~495 km, 10:45am (as of Jan 2019)
SkySat-4 5 6 7 (Block 1)
launched on Vega, 16 Sep 2016
~495 km, 10:15am (as of Jan 2019)
SkySat-8 9 10 11 12 13 (Block 2)
launched on Minotaur, 31 Oct 2017
~500 km, 1:07pm (as of Jan 2019)
SkySat-14 15 (remaining Block 2)
launched on SpaceX Falcon 9 SSO-A, 3 Dec 2018
~575 km, 10:20am (as of Jan 2019)
“generation A”
“generation C”
Notes: Slide for compositions – download guide from here:
https://www.dropbox.com/sh/cwlero9tqxyzsws/AADkcxEn29D0cH6QCMesLWwJa?dl=0

## Slide 5
focal planes shown as projected to the ground
These are the SkySat focal planes
OLD
CURRENT
From SkySat-1 to SkySat-4
From SkySat-5 to SkySat-15
Detector 2
PAN
blue
green
red
NIR
Detector 1
PAN
blue
green
red
NIR
Detector 3
PAN
blue
green
red
NIR
Detector 3
PAN
blue
green
red
NIR
Detector 2
PAN
blue
green
red
NIR
Detector 1
PAN
blue
green
red
NIR

## Slide 6
BORESIGHT CALIBRATION TECHNIQUES

## Slide 7
“Telescope boresight definition”
The telescope z axis is the boresight
y
3
2
1
Z
X
+x points along the open door
+z points down to Earth
(boresight)
It’s how the interior orientation couples/connects to the exterior orientation.
SPOILER ALERT: IT’S A ROTATION.

## Slide 8
pre-launch guess for the boresight is only within 5-10 milliradians
altitude of 575 km (for SkySat-14, 15) magnifies the error to a few kms
first images reveal the magnitude and direction of the bias
By comparing a feature to its projected coordinates, initially SkySat-14 had a
6.8 km offset
In the beginning, there’s always a big bias
actual Google Earth screenshot from SkySat-14 calibration work

## Slide 9
185 km
Landsat 8 tile
bands 4, 3, and 2
initial bias is tiny compared to Landsat extent
⇒ mistargeted SkySat imagery will be present in the Landsat tile*†
* unless you’re near an edge… then use two tiles!
† unless you’re near a corner… then use four tiles!
Phoenix, AZ
Landsat-8 has a wider swath than SkySats
C gen SkySat footprint, 6.7 km wide at nadir

## Slide 10
full, raw detector image is the
PAN j2k on top
MS j2k on bottom
full resolution SkySat-4 image of Phoenix
PAN
B
G
R
N
Registering SkySat to Landsat is tricky
Byron developed “mock orthorectification” to register raw SkySat frames to Landsat-8 PAN tiles

## Slide 11
full resolution SkySat-4 image of Phoenix
downsampled SkySat-4 image of Phoenix
Registering SkySat to Landsat is tricky
Byron developed “mock orthorectification” to register raw SkySat frames to Landsat-8 PAN tiles
downsample factor =
15 meters (ortho pixel size)
0.903 meters at nadir (SkySat-4 raw pixel size)

## Slide 12
orthorectify just the corners using SRTM3 DEM into UTM…
…then use those corner coordinates to warp the image
full resolution SkySat-4 image of Phoenix
It’s “mock orthrectification” because I’m ignoring the terrain in the middle!
downsampled SkySat-4 image of Phoenix
Registering SkySat to Landsat is tricky
Byron developed “mock orthorectification” to register raw SkySat frames to Landsat-8 PAN tiles
“mock orthorectified” SkySat-4 image of Phoenix

## Slide 13
Each detector in every frame has a geolocation error
s112_20181219T102424Z
projected location
true location
local vertical coordinate system
the
SkySat-14
collect with the 6.8 km bias from earlier
ten frames, evenly spaced along the imaging event, were coarsely marked against a Landsat-8 PAN tile
4824.03
nadir-projected meters
collect average
boresight coordinate system
(boresight x)
(boresight y)

## Slide 14
Multiple collects fully describe the pointing error
(prelaunch) boresight coordinate system
SkySat-14
Many random factors perturb the pointing of individual collects
It takes a statistical approach to reveal the orientation of the true boresight frame
Actual SkySat-14 dataset used to fit the first post launch boresight, containing 4 collects

## Slide 15
A least squares fit determines what additional rotations would minimize the pointing error.
Those same rotations are applied to GNC’s boresight definition, the “boresight-to-principal” quaternion.
Care is taken to compute cost in a way that respects yaw.
(translation: it’s easy to write cost functions that ignore yaw!)
Rotate into a better boresight
3
2
1
yaw
(boresight z)
roll
(boresight x)
pitch
(boresight y)
x
y
z

## Slide 16
Ending CE90 is determined by the spread
(prelaunch) boresight coordinate system
SkySat-14
Depending on how far along the GNC calibrations are:
gyroscopes
star trackers
the ending CE90 could be in the 1s of km, or 10s of meters
In this SkySat-14 example, GNC was quite far along, as the ending CE90 was only
29 meters at nadir
Actual SkySat-14 dataset used to fit the first post launch boresight, containing 4 collects

## Slide 17
INTERIOR CALIBRATION TECHNIQUES

## Slide 18
The interior orientation is where the detectors live
translation
(2 components)
rotation angles
(3 angles)
pivot point for all three angles is the center of the top half
ppx
horizontal pixel size
ppy
vertical pixel size
pixel pitch
(2 components)
2+3+2 = 7 degrees of freedom for each detector

## Slide 19
These are the SkySat focal planes
no GCPs!
Pléiades-1A/B georeferencing not modified
Pléiades-1A/B
(0.5 meter GSD, 10 meter CE90)
(12 meter postings, 4 meter accuracy)
REFERENCE ORTHO

## Slide 20
The high quality reference ortho looks like this
| Somalia1
a 10 km x 10 km reference image from Pléiades-1A, orthorectified with WorldDEM
Finely patterned ground cover.
It’s easy to make tie points with this scene content.
Somalia1
9.440416°N, 48.414754°E

## Slide 21
MATLAB orthorectifies the SkySat candidate images
It must be MATLAB!
the SkySat imageToGround, groundToImage transforms are coded in MATLAB!
SkySat-14
(1.038 meter GSD, ~30 meter CE90)
(12 meter postings, 4 meter accuracy) same WorldDEM tile as before!
SkySat detector orthos

## Slide 22
This is real orthorectification… terrain is most definitely being taken into account!
Orthorectified SkySat detector images look like this
for correlation to the reference ortho, raw SkySat detector images are orthorectified using the same WorldDEM terrain model as the Pléiades reference
s103_20161025T071412Z, raw
orthorectified

## Slide 23
A single frame reveals the issues
A single SkySat frame of s103_20161025T071412Z
frame = 300
Three detectors at the same frame-time
Tie points between the SkySat and Pléiades images provide feedback for geometric calibration

## Slide 24
A grid of tie points are found in all three detectors
17 x 17 x 3 = 867 total tie points
found between the SkySat detectors and Pléiades reference
17 rows
17 columns

## Slide 25
Immediately after correlation, a bias is present
In this example, a bias of ~48 meters at nadir is superimposed on the interior error
CE90 = 80.02
nadir projected meters
actual SkySat-14 interior error plot
SkySat-14
At first, a bias is present that obscures the interior error

## Slide 26
changing the pose in a least squares sense removes all error that could be exterior
CE90 = 37.41
nadir projected meters
actual SkySat-14 interior error plot
SkySat-14
Removing the bias reveals the interior error

## Slide 27
fitting the interior parameters, including pixel pitch dimensions, yields a subpixel interior
CE90 = 0.356
nadir projected meters
CE90 ≈ 0.343
pixels at nadir (!)
actual SkySat-14 interior error plot
SkySat-14
Good tie points yield sub-pixel results

## Slide 28
CONCLUSIONS

## Slide 29
On-orbit geometric calibration is crucial:
  Good boresight provides good geolocation, targeting, orthorectification;
  good interior prevents shear between detectors, enables good mosaicking.
CONCLUSIONS