## Slide 1: Geospatial Data Accuracy and the New Mapping Accuracy Standard: New Era Session #35 Dr. Qassim Abdullah, Woolpert, Inc. Pierre Le Roux, Aerometric, Inc. Becky Morton, Towill, Inc.

## Slide 2: New ASPRS Positional Accuracy Standards for Digital Geospatial Data Drafting Committee: Chair: Douglas L. Smith, David C. Smith & Associates, Inc. Dr. Qassim A. Abdullah, Woolpert, Inc. Dr. David Maune, Dewberry Karl Hans Heidemann, USGS REVISION 7, VERSION 1 NOVEMBER 14, 2014 (FINAL BOARD APPROVAED Version)

## Slide 3: New ASPRS Positional Accuracy Standards for Digital Geospatial Data
  Replaces:
    ASPRS Accuracy Standards for Large-Scale Maps (1990)
    ASPRS Guidelines, Vertical Accuracy Reporting for Lidar Data (2004)
  Developed by:
    ASPRS Map Accuracy Standards Working Group, PAD, PDAD and LIDAR joint committee for map accuracy standard update
  In Final Approved Version
    REVISION 7, VERSION 1, Nov. 14, 2014
    Approved and adopted by ASPRS during the board meeting on Monday Nov. 17, 2014 in Denver during ASPRS 2014 PECORA conference

## Slide 4: New Standard for a New Era
Motivation Behind the New Standard:
Legacy map accuracy standards, such as the ASPRS 1990 standard and the NMAS of 1947, are outdated. (over 30 years since ASPRS1990 was written)
Many of the data acquisition and mapping technologies that these standards were based on are no longer used.
More recent advances in mapping technologies can now produce better quality and higher accuracy geospatial products and maps.
Legacy map accuracy standards were designed to deal with plotted or drawn maps as the only medium to represent geospatial data.

## Slide 5: New Standard for a New Era
Within the past two decades (during the transition period between the hardcopy and softcopy mapping environments), most standard measures for relating GSD and map scale to the final mapping accuracy were inherited from photogrammetric practices using scanned film.
New mapping processes and methodologies have become much more sophisticated with advances in technology and advances in our knowledge of mapping processes and mathematical modeling.
Mapping accuracy can no longer be associated with the camera geometry and flying altitude alone (focal length, xp, yp, B/H ratio, etc.).

## Slide 6: New Standard for a New Era
New map accuracy is influenced by many factors such as:
  the quality of camera calibration parameters;
  quality and size of a Charged Coupled Device (CCD) used in the digital camera CCD array;
  amount of imagery overlap;
  quality of parallax determination or photo measurements;
  quality of the GPS signal;
  quality and density of ground controls;
  quality of the aerial triangulation solution;
  capability of the processing software to handle GPS drift and shift;
  capability of the processing software to handle camera self-calibration,
  the digital terrain model used for the production of orthoimagery.
.

## Slide 7: New Standard for a New Era
These factors can vary widely from project to project, depending on the sensor used and specific methodology. For these reasons, existing accuracy measures based on map scale, film scale, GSD, c-factor and scanning resolution no longer apply to current geospatial mapping practices.
Elevation products from the new technologies and active sensors such as lidar and IFSAR are not considered by the legacy mapping standards. New accuracy standards are needed to address elevation products derived from these technologies.

## Slide 8: ASPRS Positional Accuracy Standards for Digital Geospatial Data
  Applicability:
    Defines specific accuracy classes and associated RMSE thresholds for digital orthoimagery, digital planimetric data, and digital elevation data
    Intended to be technology independent
    Limited to accuracy thresholds and testing methodologies for any mapping applications, and to meet immediate shortcomings in the outdated 1990 and 2004 standards
    Is not intended to cover classification accuracy of thematic maps
    Does not specify the best practices or methodologies needed to meet the accuracy thresholds
  Includes:
    Glossary, Symbols, examples, conversion to legacy standards

## Slide 9: New Standard Highlights
  Positional Accuracy Thresholds which are independent of published GSD, map scale or contour interval
    digital orthoimagery
    digital elevation data
  Additional Accuracy Measures
    aerial triangulation accuracy,
    Ground controls accuracy,
    orthoimagery seam lines accuracy,
    lidar relative swath-to-swath accuracy,
    recommended minimum Nominal Pulse Density (NPD)
    horizontal accuracy of elevation data,
    delineation of low confidence areas for vertical data
    required number and spatial distribution of QA/QC check points based on project area

## Slide 10: New Standard Highlights
  Positional Accuracy Thresholds which are independent of published GSD, map scale or contour interval
    digital orthoimagery
    digital elevation data
  Additional Accuracy Measures
    aerial triangulation accuracy,
    Ground controls accuracy,
    orthoimagery seam lines accuracy,
    lidar relative swath-to-swath accuracy,
    recommended minimum Nominal Pulse Density (NPD)
    horizontal accuracy of elevation data,
    delineation of low confidence areas for vertical data
    required number and spatial distribution of QA/QC check points based on project area

## Slide 11: New Standard Highlights
  It is All Metric!
  Unlimited Horizontal Accuracy Classes:
Horizontal Accuracy Class | RMSEx and RMSEy (cm) | RMSEr (cm) | Horizontal Accuracy at 95% Confidence Level (cm) | Orthoimagery Mosaic Seamline Mismatch (cm)
X-cm | ≤X | ≤1.41*X | ≤2.45*X | ≤ 2*X
Horizontal Accuracy Standards for Geospatial Data

## Slide 12
Horizontal Accuracy Class RMSEx and RMSEy (cm) | RMSEr (cm) | Orthoimage Mosaic Seamline Maximum Mismatch (cm) | Horizontal Accuracy at the 95% Confidence Level (cm)
0.63 | 0.9 | 1.3 | 1.5
1.25 | 1.8 | 2.5 | 3.1
2.50 | 3.5 | 5.0 | 6.1
5.00 | 7.1 | 10.0 | 12.2
7.50 | 10.6 | 15.0 | 18.4
10.00 | 14.1 | 20.0 | 24.5
12.50 | 17.7 | 25.0 | 30.6
15.00 | 21.2 | 30.0 | 36.7
17.50 | 24.7 | 35.0 | 42.8
20.00 | 28.3 | 40.0 | 49.0
22.50 | 31.8 | 45.0 | 55.1
25.00 | 35.4 | 50.0 | 61.2
27.50 | 38.9 | 55.0 | 67.3
30.00 | 42.4 | 60.0 | 73.4
45.00 | 63.6 | 90.0 | 110.1
60.00 | 84.9 | 120.0 | 146.9
75.00 | 106.1 | 150.0 | 183.6
100.00 | 141.4 | 200.0 | 244.8
150.00 | 212.1 | 300.0 | 367.2
200.00 | 282.8 | 400.0 | 489.5
250.00 | 353.6 | 500.0 | 611.9
300.00 | 424.3 | 600.0 | 734.3
500.00 | 707.1 | 1000.0 | 1223.9
1000.00 | 1414.2 | 2000.0 | 2447.7
Common Horizontal Accuracy Classes according to the new standard[1]

## Slide 13
Common Orthoimagery Pixel Sizes | Associated Map Scale | ASPRS 1990 Accuracy Class | Associated Horizontal Accuracy According to Legacy ASPRS 1990 Standard | 
 |  |  | RMSEx and RMSEy (cm) | RMSEx and RMSEy in terms of pixels
0.625 cm | 1:50 | 1 | 1.3 | 2-pixels
 |  | 2 | 2.5 | 4-pixels
 |  | 3 | 3.8 | 6-pixels
1.25 cm | 1:100 | 1 | 2.5 | 2-pixels
 |  | 2 | 5.0 | 4-pixels
 |  | 3 | 7.5 | 6-pixels
2.5 cm | 1:200 | 1 | 5.0 | 2-pixels
 |  | 2 | 10.0 | 4-pixels
 |  | 3 | 15.0 | 6-pixels
5 cm | 1:400 | 1 | 10.0 | 2-pixels
 |  | 2 | 20.0 | 4-pixels
 |  | 3 | 30.0 | 6-pixels
7.5 cm | 1:600 | 1 | 15.0 | 2-pixels
 |  | 2 | 30.0 | 4-pixels
 |  | 3 | 45.0 | 6-pixels
15 cm | 1:1,200 | 1 | 30.0 | 2-pixels
 |  | 2 | 60.0 | 4-pixels
 |  | 3 | 90.0 | 6-pixels
Examples on Horizontal Accuracy for Digital Orthoimagery interpreted from ASPRS 1990 Legacy Standard.

## Slide 14
Common Orthoimagery Pixel Sizes | Recommended Horizontal Accuracy Class RMSEx and RMSEy (cm) | Orthoimage RMSEx and RMSEy in terms of pixels | Recommended use
1.25 cm | ≤1.3 | ≤1-pixel | Highest accuracy work
 | 2.5 | 2-pixels | Standard Mapping and GIS work
 | ≥3.8 | ≥3-pixels | Visualization and less accurate work
2.5 cm | ≤2.5 | ≤1-pixel | Highest accuracy work
 | 5.0 | 2-pixels | Standard Mapping and GIS work
 | ≥7.5 | ≥3-pixels | Visualization and less accurate work
5 cm | ≤5.0 | ≤1-pixel | Highest accuracy work
 | 10.0 | 2-pixels | Standard Mapping and GIS work
 | ≥15.0 | ≥3-pixels | Visualization and less accurate work
7.5 cm | ≤7.5 | ≤1-pixel | Highest accuracy work
 | 15.0 | 2-pixels | Standard Mapping and GIS work
 | ≥22.5 | ≥3-pixels | Visualization and less accurate work
15 cm | ≤15.0 | ≤1-pixel | Highest accuracy work
 | 30.0 | 2-pixels | Standard Mapping and GIS work
 | ≥45.0 | ≥3-pixels | Visualization and less accurate work
Digital Orthoimagery Accuracy Examples for Current Large and Medium Format Metric Cameras

## Slide 15: Horizontal Accuracy/Quality Examples for High Accuracy Digital Planimetric Data
ASPRS 2014 |  |  |  | Equivalent to map scale in |  | Equivalent to map scale in NMAS
Horizontal Accuracy Class RMSEx and RMSEy (cm) | RMSEr (cm) | Horizontal Accuracy at the 95% Confidence Level (cm) | Approximate GSD of Source Imagery (cm) | ASPRS 1990 Class 1 | ASPRS 1990 Class 2 | 
0.63 | 0.9 | 1.5 | 0.31 to 0.63 | 1:25 | 1:12.5 | 1:16
1.25 | 1.8 | 3.1 | 0.63 to 1.25 | 1:50 | 1:25 | 1:32
2.5 | 3.5 | 6.1 | 1.25 to 2.5 | 1:100 | 1:50 | 1:63
5.0 | 7.1 | 12.2 | 2.5 to 5.0 | 1:200 | 1:100 | 1:127
7.5 | 10.6 | 18.4 | 3.8 to 7.5 | 1:300 | 1:150 | 1:190
10.0 | 14.1 | 24.5 | 5.0 to 10.0 | 1:400 | 1:200 | 1:253
12.5 | 17.7 | 30.6 | 6.3 to12.5 | 1:500 | 1:250 | 1:317
15.0 | 21.2 | 36.7 | 7.5 to 15.0 | 1:600 | 1:300 | 1:380
17.5 | 24.7 | 42.8 | 8.8 to 17.5 | 1:700 | 1:350 | 1:444
20.0 | 28.3 | 49.0 | 10.0 to 20.0 | 1:800 | 1:400 | 1:507
22.5 | 31.8 | 55.1 | 11.3 to 22.5 | 1:900 | 1:450 | 1:570
25.0 | 35.4 | 61.2 | 12.5 to 25.0 | 1:1000 | 1:500 | 1:634
27.5 | 38.9 | 67.3 | 13.8 to 27.5 | 1:1100 | 1:550 | 1:697
30.0 | 42.4 | 73.4 | 15.0 to 30.0 | 1:1200 | 1:600 | 1:760

## Slide 16: New Standard Highlights
  Unlimited Vertical Accuracy Classes:
Vertical Accuracy Class | Absolute Accuracy |  |  | Relative Accuracy (where applicable) |  | 
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) | VVA at 95th Percentile (cm) | Within- Swath Hard Surface Repeatability (Max Diff) (cm) | Swath-to-Swath Non-Vegetated Terrain (RMSDz) (cm) | Swath-to-Swath Non-Vegetated Terrain (Max Diff) (cm)
X-cm | ≤X | ≤1.96*X | ≤3.00*X | ≤0.60*X | ≤0.80*X | ≤1.60*X
Vertical Accuracy Standards for Digital Elevation Data

## Slide 17: Vertical Accuracy/Quality Examples for Digital Elevation Data
Vertical Accuracy Class | Absolute Accuracy |  |  | Relative Accuracy (where applicable) |  | 
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) | VVA at 95th Percentile (cm) | Within-Swath Hard Surface Repeatability (Max Diff) (cm) | Swath-to-Swath Non-Veg Terrain (RMSDz) (cm) | Swath-to-Swath Non-Veg Terrain (Max Diff) (cm)
1-cm | 1.0 | 2.0 | 3 | 0.6 | 0.8 | 1.6
2.5-cm | 2.5 | 4.9 | 7.5 | 1.5 | 2 | 4
5-cm | 5.0 | 9.8 | 15 | 3 | 4 | 8
10-cm | 10.0 | 19.6 | 30 | 6 | 8 | 16
15-cm | 15.0 | 29.4 | 45 | 9 | 12 | 24
20-cm | 20.0 | 39.2 | 60 | 12 | 16 | 32
33.3-cm | 33.3 | 65.3 | 100 | 20 | 26.7 | 53.3
66.7-cm | 66.7 | 130.7 | 200 | 40 | 53.3 | 106.7
100-cm | 100.0 | 196.0 | 300 | 60 | 80 | 160
333.3-cm | 333.3 | 653.3 | 1000 | 200 | 266.7 | 533.3

## Slide 18: Vertical accuracy of the new ASPRS 2014 standard compared with legacy standards
Vertical Accuracy Class | RMSEz Non-Vegetated (cm) | Equivalent Class 1 contour interval per ASPRS 1990 (cm) | Equivalent Class 2 contour interval per ASPRS 1990 (cm) | Equivalent contour interval per NMAS (cm)
1-cm | 1.0 | 3.0 | 1.5 | 3.29
2.5-cm | 2.5 | 7.5 | 3.8 | 8.22
5-cm | 5.0 | 15.0 | 7.5 | 16.45
10-cm | 10.0 | 30.0 | 15.0 | 32.90
15-cm | 15.0 | 45.0 | 22.5 | 49.35
20-cm | 20.0 | 60.0 | 30.0 | 65.80
33.3-cm | 33.3 | 99.9 | 50.0 | 109.55
66.7-cm | 66.7 | 200.1 | 100.1 | 219.43
100-cm | 100.0 | 300.0 | 150.0 | 328.98
333.3-cm | 333.3 | 999.9 | 500.0 | 1096.49

## Slide 19: Examples on Vertical Accuracy and Recommended Lidar Point Density for Digital Elevation Data according to the new ASPRS 2014 standard
Vertical Accuracy Class | Absolute Accuracy |  | Recommended Minimum NPD (pts/m2) | Recommended Maximum NPS7 (m)
 | RMSEz Non-Vegetated (cm) | NVA at 95% Confidence Level (cm) |  | 
1-cm | 1.0 | 2.0 | ≥20 | ≤0.22
2.5-cm | 2.5 | 4.9 | 16 | 0.25
5-cm | 5.0 | 9.8 | 8 | 0.35
10-cm | 10.0 | 19.6 | 2 | 0.71
15-cm | 15.0 | 29.4 | 1 | 1.0
20-cm | 20.0 | 39.2 | 0.5 | 1.4
33.3-cm | 33.3 | 65.3 | 0.25 | 2.0
66.7-cm | 66.7 | 130.7 | 0.1 | 3.2
100-cm | 100.0 | 196.0 | 0.05 | 4.5
333.3-cm | 333.3 | 653.3 | 0.01 | 10.0

## Slide 20: Horizontal accuracy requirements for elevation data
Photogrammetric elevation data:, the horizontal accuracy equates to the horizontal accuracy class that would apply to planimetric data or digital orthoimagery produced from the same source imagery, using the same aerial triangulation/INS solution.
Lidar elevation data: use the following formula:

## Slide 21: Expected horizontal errors (RMSEr) for Lidar data in terms of flying altitude
Altitude (m) | Positional RMSEr (cm) |  | Altitude (m) | Positional RMSEr (cm)
500 | 13.1 |  | 3,000 | 41.6
1,000 | 17.5 |  | 3,500 | 48.0
1,500 | 23.0 |  | 4,000 | 54.5
2,000 | 29.0 |  | 4,500 | 61.1
2,500 | 35.2 |  | 5,000 | 67.6

## Slide 22: Low Confidence Areas in Lidar Dataset
Vertical Accuracy Class | Recommended Project Min NPD (pts/m2) (Max NPS (m)) | Recommended Low Confidence Min NGPD (pts/m2) (Max NGPS (m)) | Search Radius and Cell Size for Computing NGPD (m) | Low Confidence Polygons Min Area (acres (m2))
1-cm | ≥20 (≤0.22) | ≥5 (≤0.45) | 0.67 | 0.5 (2,000)
2.5-cm | 16 (0.25) | 4 (0.50) | 0.75 | 1 (4,000)
5-cm | 8 (0.35) | 2 (0.71) | 1.06 | 2 (8,000)
10-cm | 2 (0.71) | 0.5 (1.41) | 2.12 | 5 (20,000)
15-cm | 1 (1.0) | 0.25 (2.0) | 3.00 | 5 (20,000)
20-cm | 0.5 (1.4) | 0.125 (2.8) | 4.24 | 5 (20,000)
33.3-cm | 0.25 (2.0) | 0.0625 (4.0) | 6.0 | 10 (40,000)
66.7-cm | 0.1 (3.2) | 0.025 (6.3) | 9.5 | 15 (60,000)
100-cm | 0.05 (4.5) | 0.0125 (8.9) | 13.4 | 20 (80,000)
333.3-cm | 0.01 (10.0) | 0.0025 (20.0) | 30.0 | 25 (100,000)

## Slide 23: Accuracy requirements for aerial triangulation and INS-based sensor orientation of digital imagery
Accuracy of aerial triangulation designed for digital planimetric data (orthoimagery and/or digital planimetric map) only:
    RMSEx(AT) or RMSEy(AT) = ½ * RMSEx(Map) or RMSEy(Map)
    RMSEz(AT) = RMSEx(Map) or RMSEy(Map) of orthoimagery
Accuracy of aerial triangulation designed for elevation data, or planimetric data (orthoimagery and/or digital planimetric map) and elevation data production:
RMSEx(AT), RMSEy(AT)or RMSEz(AT) = ½ * RMSEx(Map), RMSEy(Map)or RMSEz(DEM)

## Slide 24: Accuracy requirements for ground control used for aerial triangulation
Accuracy of ground controls designed for planimetric data (orthoimagery and/or digital planimetric map)production only:
  RMSEx or RMSEy = ¼ * RMSEx(Map) or RMSEy(Map),
  RMSEz = ½ * RMSEx(Map) or RMSEy(Map)
Accuracy of ground controls designed for elevation data, or planimetric data and elevation data production:
  RMSEx, RMSEy or RMSEz= ¼ * RMSEx(Map), RMSEy(Map) or RMSEz(DEM)

## Slide 25: Examples on Aerial Traingulation and Ground Control Accuracy
Product Accuracy (RMSEx, RMSEy) (cm) | A/T Accuracy |  | Ground Control Accuracy | 
 | RMSEx and RMSEy (cm) | RMSEz (cm) | RMSEx and RMSEy (cm) | RMSEz (cm)
50 | 25 | 50 | 12.5 | 25
Product Accuracy (RMSEx, RMSEy, or RMSEz) (cm) | A/T Accuracy |  | Ground Control Accuracy | 
 | RMSEx and RMSEy (cm) | RMSEz (cm) | RMSEx and RMSEy (cm) | RMSEz (cm)
50 | 25 | 25 | 12.5 | 12.5
Aerial Triangulation and Ground Control Accuracy Requirements,
Orthoimagery and/or Planimetric Data and Elevation Data
Aerial Triangulation and Ground Control Accuracy Requirements,
Orthoimagery and/or Planimetric Data Only

## Slide 26: Reporting Horizontal Accuracy
“This data set was tested to meet ASPRS Positional Accuracy Standards for Digital Geospatial Data (2014) for a ___ (cm) RMSEx / RMSEy Horizontal Accuracy Class. Actual positional accuracy was found to be RMSEx = ___ (cm) and RMSEy = ___ cm which equates to +/- ___ at 95% confidence level.”
“This data set was produced to meet ASPRS Positional Accuracy Standards for Digital Geospatial Data (2014) for a ___ (cm) RMSEx / RMSEy Horizontal Accuracy Class which equates to +/- ___ cm at a 95% confidence level.”

## Slide 27: Reporting Vertical Accuracy
“This data set was tested to meet ASPRS Positional Accuracy Standards for Digital Geospatial Data (2014) for a___ (cm) RMSEz Vertical Accuracy Class. Actual NVA accuracy was found to be RMSEz = ___ cm, equating to +/- ___ at 95% confidence level. Actual VVA accuracy was found to be +/- ___ cm at the 95% percentile.”
“This data set was produced to meet ASPRS Positional Accuracy Standards for Digital Geospatial Data (2014) for a ___ cm RMSEz Vertical Accuracy Class equating to NVA =+/-___cm at 95% confidence level and VVA =+/-___cm at the 95% percentile

## Slide 28: Recommended Number of Check Points Based on Area
Project Area (Square Kilometers) | Horizontal Accuracy Testing of Orthoimagery and Planimetrics | Vertical and Horizontal Accuracy Testing of Elevation Data sets |  | 
 | Total Number of Static 2D/3D Check Points (clearly-defined points) | Number of Static 3D Check Points in NVA | Number of Static 3D Check Points in VVA | Total Number of Static 3D Check Points
≤500 | 20 | 20 | 5 | 25
501-750 | 25 | 20 | 10 | 30
751-1000 | 30 | 25 | 15 | 40
1001-1250 | 35 | 30 | 20 | 50
1251-1500 | 40 | 35 | 25 | 60
1501-1750 | 45 | 40 | 30 | 70
1751-2000 | 50 | 45 | 35 | 80
2001-2250 | 55 | 50 | 40 | 90
2251-2500 | 60 | 55 | 45 | 100

## Slide 29: New Standard Highlights
  Not Yet Addressed:
    Methodologies for accuracy assessment of linear features (as opposed to well defined points)
    Rigorous total propagated uncertainty (TPU) modeling (as opposed to -- or in addition to – ground truthing against independent data sources)
    Robust statistics for data sets that do not meet the criteria for normally distributed data and therefore cannot be rigorously assessed using the statistical methods specified herein
    Image quality factors, such as edge definition and other characteristics
    Robust assessment of check point distribution and density
    Alternate methodologies to TIN interpolation for vertical accuracy assessment

## Slide 30: Example on Applying the New Standard
User asked for orthoimagery with GSD =10 cm ortho, what specifications he/she needs to ask for?
Answer:
1) According to the legacy standard of 1990, most probably will be: Horizontal Accuracy RMSE = 20 cm (2 pixels) class I, Map scale = 1:800
2) According to the new Standard:
- RMSE = 10 cm (highest obtainable/"highest accuracy work“, entails ground controls accurate to 2.5 cm and very accurate workflow)
- RMSE = 20 cm ( comparable to 1990)
Practical specs: RMSE = 15 cm, no scale to be assigned

## Slide 31: The Standard Web Site
The final standard document is posted on the web page:
http://www.asprs.org/PAD-Division/Map-Accuracy-Standards-Working-Group.html

## Slide 32: Thank You!